# General Description

A template defines the top-level entity/architecture. The template contains place-holders, to inject synthesizable code, and simulate the behaviour on the rising edge of the clock, and receipt of a reset signal.
 The process state-machine maps to a concurrent (combinatorial) VHDL process clled 'beginCycle', described in the architecture. Synchronous state-machines map to procedure declarations in 'beginCycle'.

The process state-machine does not have a state-machine progress control variable. It is translated to sequential code which is evaluated, from beginning to end, on the rising clock edge.

Synchronous state-machines are evaluated using a procedure call from the process state-machine. This means the synchronous state-machines makes one transition per clock tick.

The current approach translates Event-B integer and boolean variables/constants as follows,

Variables map to signals:
Integer variables map to signals of type Integer.
Boolean variables map to signals of type std_out.

Integer constants map to constant Integer types.
Boolean constants map to constant std_out types ???

Nested state-machines are flattened during translation.
There are no parallel state-machines.

# Translation of Component Diagram Elements

Top-level Diagram
Name	No mapping to VHDL. Ignored in translation.
Variables	Variables (a) associated with connectors become signals in the entity port declaration. / Variables associated with incoming connectors also map to 'signals' in the the cycle process sensitivity list.
Invariants	Map to typing information for the variables in (a) the entity port declaration. / Initialisations / Map to initialisations of the variables in (a).
Sets	No mapping to VHDL. Ignored in translation.
Constants	Map to VHDL Constants (b) declared and initialised in the architecture declarative section.
Axioms	Contribute to mapping of (b).
Components	Map to entity/architecture descriptions.
Name	Maps to the entity declaration 'name'.
Variables	Map to VHDL signals (c) declared and initialised in the architecture declarative section.
Invariants	Contribute to mapping of (c).
Initialisations	Contribute to mapping of (c).
Sets	No mapping to VHDL. Ignored in translation.
Constants	Map to VHDL Constants (d) declared and initialised in the architecture declarative section.
Axioms	Contribute to mapping of (d).
Port-wake	No mapping to VHDL. Ignored in translation: The port-wake is simulated by the test-bench. / Variable reads are implemented using explicit assignment from signal to variable. Mapping information is obtained from the state-machine diagrams.
Self-wake	No mapping to VHDL. The self-wake is simulated by the test-bench.
Transition	No mapping to VHDL. Information is obtained from state-machine diagrams.
Operation	No mapping to VHDL. Mapping information is obtained from the state-machine diagrams.
Process state-machine	Maps to a concurrent process in the architecture. / Describes a sequence of events occurring within a single clock cycle. / A path formed by a sequence of transitions, between initial and final nodes, must be traversed in the single clock cycle. / There is a single process state-machine per component.
Name	Not used, but may map to the name of the 'cycle' process if required.
Initial node	No mapping to VHDL. Ignored in translation.
Incoming transition	No mapping to VHDL. Ignored in translation.
Outgoing transition	The top-level initial node's outgoing transition provides the entry point for the sequential behaviour. Subsequent (nested) initial nodes are removed during flattening. / Guards/Actions of initial outgoing transitions, involving a junction target, will be accumulated during flattening.
Final node	No mapping to VHDL. Ignored in translation.
Incoming transition	No mapping to VHDL (since it will be mapped as another state's outgoing transition).
Outgoing transition	No mapping to VHDL. Ignored in translation.
State	No mapping to VHDL. Removed in translation.
Incoming transition	No mapping to VHDL (since it will be mapped as another state's outgoing transition).
Outgoing transitions and elaborating events	A single outgoing transition with no guard: Action maps to an assignment (i.e. forced progress). / A single outgoing transition with a guard: maps to a branch where the guards maps to the conditions, actions map to assignments (i.e. there is potential non-progress/implicit self-transition). / Multiple outgoing transitions map to branches and sub-branches. / There is no guarantee of guard disjointness. This would need to be addressed to reflect a deterministic implementation. / Guard incompleteness is a feature of the approach, resulting in potential non-progress (i.e. an implicit self-transition). / When an event is encountered, that is referred to in a synchronous state-machine, a synchronous state-machine procedure call is created. The call (and procedure name) are based on the synchronous state-machine name. See (e).
Nested state-machine	No mapping to VHDL. Removed in translation. / A nested state-machine initial node's outgoing transitions' elaborating events should match incoming transitions (possibly defined higher in the refinement chain). The redundant transitions are removed during flattening. / There is no transition from the parent state to any other state. Transitions to states outside of the nested state-machine come directly from nested states. An exiting transition may have a junction as the target node.
Name	No mapping to VHDL.
Any	No mapping to VHDL.
Junction	No mapping to VHDL. Removed in translation. / Guards/Actions of incoming/outgoing transitions, will be accumulated during flattening. / Currently restricted to multiple incoming – single outgoing Junctions.
Fork/Join	No mapping to VHDL.
Invariant	No mapping to VHDL.
Synchronous state-machine	A synchronous state-machine maps to a procedure definition. / The events of a synchronous state-machine should elaborated in exactly one transition, in the process state-machine. This maps to a procedure call in the process state-machine implementation (calling once per clock cycle?).
Name	The procedure name is based on the synchronous state-machine name. / The procedure name (e) is do_*, where * represents the state-machine name.
Initial node	No mapping to VHDL.
Incoming transition	No mapping to VHDL.
Outgoing transition	No mapping to VHDL. Actions of the initial node's outgoing transition are ignored. Component variable initialisations are defined at the component-level.
Final node	No mapping to VHDL.
Incoming transition	No mapping to VHDL.
Outgoing transition	No mapping to VHDL.
State	Each state forms the basis of a case block (f) in the implementation.
Incoming transition	No mapping to VHDL (since it will be mapped as another state's outgoing transition).
Outgoing transitions and elaborating events	A single outgoing transition with no guard: The actions map to assignments (i.e. forced progress). / A single outgoing transition with a guard: maps to a branch, where the guards maps to conditions and actions map to assignments (note, potential non-progress/implicit self-transition). / Multiple outgoing transitions map to branches and sub-branches, also with an implicit self-transition. / There is no proof of guard disjointness, but PO's should be generated to reflect a deterministic implementation. / Guard incompleteness is a feature of the approach, resulting in potential non-progress (i.e. an implicit self-transition).
Name	Each synchronous state-machine has an enumerated type *_states representing the possible states of a state-machine progress counter, where * is the state-machine name. / Each state name maps to a value in the enumeration. / A variable * of type *_states records the current state-machine counter value. / A case block (f) is produced of the form: / case * is / each name maps to a case statement, / when name => … / for each state name in *_states. / A variable next_*, of type *_states, records the next state-machine counter value, i.e. the value of the state-machine counter after the next clock tick. / A constant init_* of type *_states records the initial value of the state-machine counter, to facilitate a reset.
Any	No mapping to VHDL.
Junction	No mapping to VHDL. Removed in translation. / Guards/Actions of incoming/outgoing transitions, will be accumulated during flattening. / Currently restricted to multiple incoming – single outgoing Junctions.
Fork/Join	No mapping to VHDL.
Nested state-machine	No mapping to VHDL. Removed in translation. / A nested state-machine initial node's outgoing transitions' elaborating events should match incoming transitions (possibly defined higher in the refinement chain). The redundant transitions are removed during flattening. / There is no transition from the parent state to any other state. Transitions to states outside of the nested state-machine come directly from nested states. An exiting transition may have a junction as the target node.
Invariant	No mapping to VHDL.
Asynchronous state-machine	No mapping to VHDL.
Connectors	Map to ports in the entity.
Name	The name of port in upper-case corresponds to a lower-case Event-B variable (g). The variable maps to a portName in a port declaration. / The portName is used to read incoming values, and write outgoing values.
Type	Not mapped to VHDL, but used to identify (g) the variable describing the port dataType in the port declaration.
Initial	Not mapped to VHDL, the variable initialisation (related to (g)) is not used in the port declaration.
Link	Maps to the mode (in/out) of the portName.